## Slide 1: The Evolution of Timekeeping
Jerry (Yuanjie) Zhao

## Slide 2: Imagine you are Robinson Crusoe…
How do you keep track of time?

## Slide 3: Sundial
Use the shadow of a stick to keep time

## Slide 4: Problem: not working at night

## Slide 5: Water clock & Hour glass

## Slide 6: Problem: less accurate than sundial
Less accurate & stable than sundial in long term
water clock: hard to keep water drip at a constant rate
hour glass: need human to flip hour glass and count the hours
Extra Problems of sundial
Max accuracy is minute, no way to subdivide minute in a sundial
Length of an hour changes over seasons
An hour in the summer is much longer than in the winter

## Slide 7: Mechanical clock (pendulum)
Escapement controls transfer of energy from power source to the counting mechanism.
Animation

## Slide 8: Problem: unreliable on boat
violent motion of sea, variations in gravity at different latitudes

## Slide 9: Mechanical clock (coiled spring)
Use spring to regulates the rotary oscillation of main wheel
video

## Slide 11: Problem: not accurate for scientists
Need more accurate clock for experiments like measuring speed of light

## Slide 12: Quartz Clock
Piezoelectric effect

## Slide 13: Quartz Clock

## Slide 14: Quartz Clock
The crystal is designed to oscillate at 32,768 Hz (215 = 32768).
Each time a 16-bit counter reaches 32,768, it sends an output and you get a second

## Slide 15: Problem: still not stable enough
Different crystals resonate at slightly different frequency.
Resonant frequency depends on temperature.
Typical quartz crystal clocks drift 1.73 seconds per day.

## Slide 16: Atomic Clock
Transition between energy states emits radiation at definite frequency.
All atoms resonate at extremely consistent frequencies

## Slide 17: Atomic Clock
Cesium clock drifts 8.46ns per day.
1 second = 9,192,631,770 cycles of a Cesium atomic clock

## Slide 18: Appendix: How atomic clock works

## Slide 19: Appendix: How atomic clock works

## Slide 20: Future Investigations
Can we build a clock that drifts less than 1s for the entire lifespan of our universe?
How to accurately transfer time between such precise clocks?

## Slide 21: Reference
1. Hinkley, N., Sherman, J. A., Phillips, N. B., Schioppo, M., Lemke, N. D., Beloy, K., ... & Ludlow, A. D. (2013). An atomic clock with 10− 18 instability. Science, 1240420.
2. Ives, H. E., & Stilwell, G. R. (1938). An experimental study of the rate of a moving atomic clock. JOSA, 28(7), 215-226.
3. Wikipedia contributors. (2018, September 27). History of timekeeping devices. In Wikipedia, The Free Encyclopedia. Retrieved 16:44, October 11, 2018, from
https://en.wikipedia.org/w/index.php?title=History_of_timekeeping_devices&oldid=861475382
4. Wikipedia contributors. (2018, September 29). Standard time. In Wikipedia, The Free Encyclopedia. Retrieved 07:00, October 11, 2018, from
https://en.wikipedia.org/w/index.php?title=Standard_time&oldid=861687315
5. Lewandowski, W., Azoubib, J., & Klepczynski, W. J. (1999). GPS: primary tool for time transfer. Proceedings of the IEEE, 87(1), 163-172.
6. Wikipedia contributors. (2018, October 2). Time zone. In Wikipedia, The Free Encyclopedia. Retrieved 07:01, October 11, 2018, from
https://en.wikipedia.org/w/index.php?title=Time_zone&oldid=862212990
7. Alvele, B. (2018). Time Standards. Retrieved from
http://www.exactlywhatistime.com/measurement-of-time/time-standards/

## Slide 22: Reference
Image
https://hibiscusmooncrystalacademy.com/wp-content/uploads/2015/06/piezo.png
http://hyperphysics.phy-astr.gsu.edu/hbase/images/Csclock.gif
https://1.bp.blogspot.com/-3od_KZWyuYo/WKKgB9hWcEI/AAAAAAAABEg/8Y0XT_PJBAIRKkM1rbTzABKRF-rg8VoTwCLcB/s1600/piezoelectric-transducer.PNG
https://www.edumedia-sciences.com/en/media/767-mechanical-clock
https://static.makeuseof.com/wp-content/uploads/2013/04/time-clock-670x335.jpg
Video
https://www.youtube.com/watch?v=1pM6uD8nePo

## Slide 23: QA